## Slide 1: Network Security
Spring 2025

## Slide 2: TCP 3-way handshake
TCP SYN
TCP SYN/ACK
TCP ACK
When host receives a TCP SYN packet
Open sockets
Allocating resources (CPU/memory) to prepare for the connect

## Slide 3: Task 1a. SYN Flood Attack
TCP SYN
Server will allocate resources for each TCP SYN received. Will soon run out of resources
Attacker
(Trudy)
TCP SYN
TCP SYN
TCP SYN
TCP SYN
TCP SYN
TCP SYN
TCP SYN
TCP SYN
TCP SYN
TCP SYN
TCP SYN
Size of a TCP SYN Packet: 40 bytes (IP header=20b + TCP header 20b)
TCP SYN Flood attacks are very easy to perform, and a normal computer has 40 available sockets

## Slide 4: Task 1b: mitigate a SYN Flood attack: SYN Cookies
Host A
Host B
SYN:SYN=ISNA
SYN-ACK with ISNB= cookie
ACK: cookie + 1
With SYN Cookie protections are on: When Host B received a TCP SYN
It does NOT allocate resources yet
It sends a SYN Cookie
Only when host B received the SYN cookie back
Does it allocate a socket for the connection

## Slide 5
726 Broadway, 8th Floor – ITS
1 Metrotech Center, 22nd Floor
noc-its18-arin@nyu.edu
noc-cosi-arin@nyu.edu
+1-212-998-34
+1-212-998-344431
216.165.0.0/17
AS12 (128.122.0.8)

## Slide 6
Engineering.nyu.edu -> hosted by AWS
Brightspace.nyu.edu -> nyu.Brightspace.com -> AWS
Cyber.nyu.edu -> AWS
Albert.nyu.edu -> 216.165.62.30
Hosting.nyu.edu -> DigitalOcean
Stream.nyu.edu -> kltura.com -> cloudflare.net
Mail server: pphosted.com

## Slide 7: DNS Record Types
A records – IPv4 IP addres
AAAA – IPv6 IP address
TXT – “free text”, often used for email security (SPF)
CNAME – similar to alias
NS – DNS servers for the domain
MX – mail server

## Slide 8: Emails to NYU
User
Proofpoint
gmail

## Slide 9: ICMP echo request/reply
User
Google
8.8.8.8
ICMP echo request
ICMP echo reply
User1
Google
ICMP Echo request
ICMP echo reply
Lab 2 Task 2

## Slide 10: Lab 2 Task 3 – write your own traceroute program
Google DNS Server
8.8.8.8
SEED machine
Icmp ping TTL 1
Icmp ping TLL 2
..
…
….
Task 3, the sample code does not handle when there is no reply properly (program will hang)

## Slide 11: Lab 2 Task 4
User
Google
8.8.8.8
ICMP request
ICMP echo reply
Attacker
ICMP echo reply
When the user tries to ping 8.8.8.8, the user will receive two icmp echo replies: 1. is from the real google DNS
2. Is from the attacker (that’s you)
User
1.2.3.4
ICMP request
When the user tries to ping 1.2.3.4
There is no response (probably host doesn’t exist)
No reply
ICMP echo reply
Part 1
Part 3

## Slide 12
User 10.9.0.x
10.9.0.99
No reply
Attacker
(sniffing ICMP echo request)
ARP Ping (ARP Request)
Part 2

## Slide 13: TCP Port scanning (1)
TCP SYN dport 443
TCP SYN/ACK
TCP ACK
Normal process for
Port 443 is open
TCP SYN dport 443
TCP RST
Port 443 is closed
Gets a TCP RST

## Slide 14: TCP port scanning (2)
TCP SYN dport 443
ICMP destination unreachable
Networking error (route not found, host does not exist)
“Rejected” by a Firewall
ICMP destination unreachable
TCP SYN dport 443
(no response)
No response
Networking error (route not found, host does not exist)
“Drop” by a Firewall

## Slide 15: REJECT or DROP
REJECT
  Firewall is being nice, is sending a ICMP destination unreachable
DROP
  The packet is ”being sent to the bit bucket”
  Firewall is not responding at all

## Slide 16: Nmap SYN Scan vs. Connect Scan
TCP SYN dport 443
(nmap listens for a response)
SYN Scan
Nmap has elevated privilege
Can write directly to the network
TCP Connect Scan
Nmap does not have elevated privileges
Must use OS API (sockets) to open/close ports
TCP SYN dport 443
TCP SYN/ACK
TCP ACK
TCP FIN
TCP FIN/ACK
TCP ACK

## Slide 17: Nmap ACK Scan – only works on stateless firewalls
FW
TCP port 443
Flags: SYN/ACK
Flags: SYN/ACK
Attacker tries to connect to port 443
(TCP SYN will get blocked
When an attacker tries to connect to host in port 443,
It will be blocked by the FW, because it only allows outgoing
Connects to port 443, not incoming connections
Attacker connect to port 443
Using TCP ”ACK” flag only
When the attacker tries to connect to port 443,
Using TCP “ACK” packet, it will be allowed through the firewall
Becaue the firewall must allow TCP ACK to come into the network
Due to allowing port 443 to go out of the network.
If successful, the host will reply back to the attacker with a. RST packet
RST

## Slide 18: Attackers pivot to other hosts

## Slide 19: UDP Scanning
UDP DNS port 53
DNS Response
Port is open
Send a request, get a response
Port is closed
ICMP Destination unreachable is received
UDP DNS port 53
ICMP Destination Unreachable
*
* don’t get confused with TCP ICMP unreachable
UDP DNS port 53
(no response)
No response
Firewall is blocking port
Improperly formatted request
ICMP Destination unreachable limit
  Limited: 1/s in Linux or 2/s in Winodws

## Slide 20: ICMP Destination Unreachable
ICMP Destination Unreachable are limited
  Windows: 2 times / sec
  Linux 1 time / sec
  If you sent two UDP packets to two closed ports at the same time, only the first one will response. The 2nd response is DROPed
Trudy sends a broadcast request
Victim

## Slide 21: Remote Scanning vs. Agent-based scanning
Remote scanning
  Traditional scanning method
  It is very slow for UDP
Agent-based scan
  Must better and faster
  Can list all ports/services quickly
  Cost is approximately 10x more
Scanner
Target
Port scans coming from outside

## Slide 22: SYN Cookies
TCP SYN
SEQ: ISN A (random number)
ACK: 0 (literal “0”, b/c there’s no ACK flag set)
TCP SYN/ACK
SEQ: ISN B ( SYN cookie)
ACK: A+1
TCP ACK
SEQ: A+1
ACK: B+1 (SYN_cookie + 1)
When SYN Cookies are enabled
Upon receipt of a TCP SYN
The host will generate a SYN Cookie
SYN_cookie = md5(IPs,ports,slow_time,magic)
All the info is forgotten.
If a SYN_cookie is returned in the TCP ACK packet
Host will recalculate the SYN_cookie, and see if it matches the SYN_cookie from the TCP ACK
Only if the correct SYN cookie is returned, will a socket be opened.

## Slide 23: DNS Amplification/Reflection attack
attacker
victim
DNS server
DNS server
DNS server
DNS server
request
request
request
request
reply
reply
reply
reply
Source IP = Victim’s IP
TXT Record
Response size: up to 512 bytes
DNS request 60-80b
Notes: Large TXT field; forgeability UDP addresses, the availability of open resolvers, and the asymmetry of DNS requests and responses

## Slide 24: Interlude: How DNS Works
Trudy
Fake engineering.nyu.edu
For the attacker to perform a DNS cache poisoning, the attacker must:
Must respond back faster than the real DNS server (very easy if on the same network, hard if not on the same network)
Spoof the real DNS Server’s IP address (very easy)
Use the same Transaction ID & port# as the DNS packet (easy if you can read the packets, hard if you cannot read the packets)

## Slide 25: Interlude: How DNS Works
Trudy
Fake engineering.nyu.edu

## Slide 26: Interlude: How DNS Works
Trudy
Fake engineering.nyu.edu
Another victim
Fake NYU.edu NS server

## Slide 27: Cover_tcp
1. IP ID method – random 16-bit number in the IP header, used for reassembling fragmented packets.
2. SEQ# Method (32-bits)
Sender
Recipient
IP ID: “HELO” (16 bits) – IP header
Sender
Recipient
TCP SEQ#: “HELOWORD” - TCP Header
Every IP packet has a IP ID #. The sender can choose a new IP ID per packet
Every new TCP connection has a SEQ number chooses initially (called a ISN).

## Slide 28: Cover_tcp (cont)
3. ACK # Method
Sender
Recipient
Innocent Bystander
TCP SYN
SEQ: “HELLO” (in ascii)
Source IP: recipient
TCP SYN/ACK
SEQ: ISN B
ACK: “HELLO” + 1
Recipient, upon receiving “HELLO” + 1, knows that the original message was “HELLO”